## Slide 1
Internet of things capstone project:
Hotdog SEIS 785-01
Robert Driesch

## Slide 2: Project hotdog requirements
A wearable (collar based) safety device for pets to warn when the Heat Index starts to approach dangerous levels
Solicit help from neglectful owners and passers-by when a pet is in a dangerous situation
  For example: locked in a car
Fully mobile & independent solution to protect pets while in a car and not at home (e.g. no wifi)
Waterproof and wearable on a collar but yet still visible enough to indicate when a dangerous situation is present

## Slide 3: Statistics & Market Potential
A dog can succumb to Heat Stroke in under 10 minutes in a vehicle
  Temperatures (Heat Index) can quickly rise 20 to 30 degrees within a car even with the windows rolled down
No official statistics are kept of dogs injured or dead because of Heat Stroke
  News is still littered with stories every year
Estimated 70 – 80 million dogs owned in the U.S.
Appx. 37% - 47% of all households have at least one dog
Pet owners spent $60.28 Billion on products in 2015
  32% was spent on Pet Supplies and Services, continues to grow 4% annually
How much would you spend to ensure the safety of your pet??

## Slide 4: Ingredients
Particle Electron w/Breadboard
  Particle SIM Card
  Cellular Antenna
  2000mAh 3.7V LiPo Battery (rechargeable)
Sensors
  DS18B20 Waterproof Temperature Sensor
  4.7k Resistors
  Various Jumpers
Extras - Optional
  Particle Photon (instead)
  External RGB LED (e.g. NeoPixel)
  Piezo Buzzer
  Humidity Sensor
  Various Jumpers and Resistors

## Slide 5: How It Works
Temperature & Humidity sensor data is collected
  Heat Index is calculated and threat levels are determined
    Alert conditions are identified
    External events can also trigger alerts
Feedback is Generated
  RGB LED’s are set from Heat Index threat levels
    Sliding color/intensity scale from Blue to Red
  Data is published via Webhooks
  SMS Text messages are sent to owner(s) for Alert conditions
Activity is governed to minimize battery drawdown

## Slide 6: Future Improvements
Hardware
  Continue to shrink the form factor & components to make it wearable
  Develop a waterproof shell to contain the components
  Develop a recharging port for the battery
Software
  Improve algorithm to conserve power & data by controlling battery and publishing intervals
  Expand the functionality of the cellular interface (geo-location)
  Tie the data being generated into IBM’s BlueMix Suite
  Refine the external inputs (Weather Data)
Mobile App
  Make it beautiful, elegant and clean
Expand to support “Chilly Dog”